|  | ......................... pc € .............................. € .............................. External flashing light BLE 220 for optical alarm display. Tough, maintenance-free and reliable construction, xenon tubes for high visibility performance, one flash emitted per second. For optional combination with external signal horn SM, polycarbonate housing; Operating voltage 20-30 V DC; Current consumption 90 mA; enclosure rating IP 54 Size (diameter x height): 93x72mm Reflector colour: red |
| --- | --- |
|  | ......................... pc € .............................. € .............................. External signal horn SLH 220 for acoustic alarm indication. With 26 level adjustable signal sound, variable volume from 74 - 94 dB (A) at 1 m distance at 24 V. Operating voltage 10-28 V DC, Current consumption 16 mA Enclosure rating IP54 Dimensions SM: (diameter x height) 111x25.5mm, FM: 81x81x62.5 mm ( ) SM white ( ) FM ( ) Jung ST 550 alpine white ( ) Jung LS stainless steel for FM installation 62.5 deep FM sockets are required. |
|  | ......................... pc € .............................. € .............................. Signal horn with flashing light SHB 220, comprising external signal horn and external flashing light, for acoustic and optical alarm Size: 111 x 97 mm (( x H) Colour: white Reflector colour: red Installation: screw fixing Operating voltage: 20 - 30 V DC Current consumption: maximum 110 mA at 24 V DC Flash frequency: 1 Hz, ( 20 % Volume of sound: 94 dB (at 1 m distance) Enclosure rating: in accordance with DIN 40 050: IP54 |
|  | ......................... pc € .............................. € .............................. External malfunction light SLE 220 for optical display of status or alarm. Operating voltage 24 V DC; Current consumption 85 mA; Enclosure rating IP 20 Dimensions flush mounting (WxHxD) 81x81x41mm. ( ) Jung ST 550 alpine white ( ) Jung LS stainless steel |
|  | ......................... pc € .............................. € .............................. External key-operated switch SCT 320 Flush mounting – unit suitable for switch range with dimensions 55x55mm. Including flat ribbon cable to connect to a GEZE door control unit TZ32x Key-operated button with 2 switch contacts to switch the functions short-time release, for permanent unlocking, locking and alarm resetting Cover protected from sabotage With profile half cylinder Colour: ( ) anthracite ( ) white matt ( ) white aluminium Frame: none |
|  | ......................... pc € .............................. € .............................. External key-operated switch SCT 222 for authorised use of the door, connection to GEZE SecuLogic door control units, bicolour LED green/red to display status unlocked / locked, yellow LED to display status alarm key-operated button for button operation on both sides for unlocking and short-time activation / locking complete with profile cylinder and 3 keys Enclosure rating IP 54 Size (WxHxD): FM: front plate 100x110 mm; FM case 80x70x45 mm SM: 80x70x45 mm ( ) Surface Mounting: ( ) Flush Mounting: Relay board RP220 or terminal box KL220 required! |
|  | ......................... pc € .............................. € .............................. External key-operated button SCT 221 for authorised use of the door by activating the short-time unlocking with a key for installation on exterior or interior of door, FM or SM installation Enclosure rating: IP 54 Size (WxHxD) SM: 75x75x50 mm FM: 75x75x61 50mm deep FM zamac socket included. ( ) Surface Mounting: ( ) Flush Mounting: ( ) with profile half cylinder ( ) without profile half cylinder |
|  | ......................... pc € .............................. € .............................. External key-operated button SCT 220 UP for authorised use of the door by activating the short-time unlocking with a key, for installation on exterior or interior of door, FM installation complete with profile cylinder in single frame Enclosure rating: IP 20 Size (WxHxD): 81x81x62.5mm for installation 62.5 deep FM sockets are required. ( ) Jung ST 550 alpine white ( ) Jung LS stainless steel ( ) Gira E2 pure white |
|  | ......................... pc € .............................. € .............................. Escape route sign TZ 320 Illuminated emergency button – information sign FWS 320 B, FM Flush mounting – unit suitable for switch range with dimensions 55x55mm. Integrated illuminated emergency button information sign with LEDs evenly illuminated operating voltage 24 V DC Current consumption 30 mA excl. frame |
|  | ......................... pc € .............................. € .............................. Escape route sign TZ 320 Emergency buttons information sign, unlit FWS 320, FM Suitable for switch range with dimensions 55x55 mm. integrated emergency buttons indication sign, unlit excl. frame |
|  | ......................... pc € .............................. € .............................. Emergency button NOT 320 FM Illuminated emergency button with transparent, accessible cover for FM installation, complete with single frame Jung AS500 alpine white Lit with long-life LED Operating voltage: 24 V DC (+/- 10%) Current consumption: 30 mA Enclosure rating: IP20 Dimensions (W x H x D) 55 x 55 x 27 mm For installation in standard FM socket, depth 46mm ( ) Jung AS500 alpine white ( ) Jung LS990 stainless steel (with outer and inner frames) ( ) Gira E2 pure white (with outer frames) |
|  | ............................ pc € .............................. € .............................. Emergency button NOT 320 SM Illuminated emergency button with transparent, accessible cover for SM installation, complete with single frame Jung AS500 alpine white and SM cap. Lit with long-life LED Operating voltage: 24 V DC (+/- 10%) Current consumption: 30 mA Enclosure rating: IP20 Dimensions (W x H x D) 55 x 55 x 27 mm ( ) Jung AS500 alpine white ( ) Gira Profile 55 aluminium ( ) Gira Profile 55 white |
|  | ......................... pc € .............................. € .............................. Emergency button NOT 220 FM Illuminated emergency button with sealable reusable cover for FM installation, complete with single frame and sign “Emergency Exit”, Lit with long-life LED Operating voltage: 24 V DC Current consumption: 17 mA Enclosure rating: IP20 Dimensions (WxHxD) 81x81x62.5 for installation 62.5 deep FM sockets are required. ( ) Jung ST 550 alpine white ( ) Jung LS stainless steel ( ) Gira E2 pure white |
|  | ......................... pc € .............................. € .............................. Emergency button NOT 220 SM (aluminium) Illuminated emergency button with sealable reusable cover for SM installation, complete with sign “Emergency Exit” Aluminium housing Lit with long-life LED Operating voltage: 24 V DC Current consumption: 17 mA Enclosure rating: IP20 Dimensions (WxHxD): 72x147x75.5mm ( ) stainless steel design ( ) green RAL 6032 ( ) custom colours to RAL |
|  | ......................... pc € .............................. € .............................. Emergency button NOT 220 AP (plastic) Illuminated emergency button with sealable reusable cover for SM installation, complete with sign “Emergency Exit”, Plastic housing, Lit with long-life LED. Operating voltage: 24 V DC Current consumption: 17 mA Enclosure rating: IP 65 Colour: light grey Dimensions (WxHxD): 94x94x81/122 |
|  | ......................... pc € .............................. € .............................. Bracket for sign “Emergency Button” Plexiglas with spacers Size (WxHxD): 100x100x21 mm |
|  | ......................... pc € .............................. € .............................. Emergency Power Supply: Uninterruptible power supply 230 V AC incl. PC interface, monitoring software and quadruple optical status display, with maintenance-free lead batteries, delivered in switch cabinet with pivoting front door, with standard double-bit key lock powder-coated metal, Incl. wall attachment set Colour: RAL 7032 Operating voltage: 230 V AC, Output voltage: 230 V AC Enclosure rating: IP 64 ( ) GEZE USV 700 Emergency Power Supply: Power: 700 VA Size: 380x600x210 (HxWxD) ( ) GEZE USV 1000 Emergency Power Supply: Power: 1000 VA Size: 380x600x210 (HxWxD) |
|  | ......................... pc € .............................. € .............................. Relay Board RP 220 for universal use in conjunction with TZ 320, to connect access control systems, key-operated button, motor locks and much more. |
|  | ......................... pc € .............................. € .............................. Logbook for documentation of acceptance and services |
|  | ......................... pc € .............................. € .............................. Numerical code lock Toplock CTS V, in metal housing, with vandal-proof metal keyboard, for input of 1 to 6 digit codes, incl. separate evaluation unit, on separate mounting plate potential free relay output, pulse 1 sec. Operating voltage: 230V AC Enclosure rating: IP 65 Enclosure rating of the evaluation unit: IP 43 Dimensions of evaluation unit: 188x110x40 (WxHxD) ( ) CTS V (80x80x15 mm WxHxD) ( ) CTS BV illuminated (60x126x23 mm WxHxD) |
|  | ......................... pc € .............................. € .............................. Door terminal TT 220 in bus technology for parallel operation and display to door control units TZ 320, to secure an escape and rescue route including in opposite direction. Also for additional securing of extra wide door systems. Fittings: integrated, illuminated emergency button, integrated 3 LED displays for door status - door locked, locked by burglary alarm system - door unlocked, unlocked by timer - door open / closed. - alarm and pre-alarm, integrated key-operated button for - unlocking - short-time unlocking - locking - alarm resetting, integrated, differentiated acoustic alarm to indicate the pre-alarm or the actuation of the emergency button/alarm actuation by danger alarm system. integrated sabotage protection, Operating voltage: 24 V DC (supplied by TZ 220) connection to TZ 220 using 2-wire bus. Door terminal TT 220 Dimensions (WxHxD): ( ) Surface Mounting: 72x350x75.5 mm ( ) Flush Mounting: ( ) double frame 81x151x62.5 mm ( ) triple frame 81x223x62.5 mm ( ) quadruple frame 81x295x62.5 mm Version: ( ) Surface Mounting: ( ) aluminium housing in shade RAL 6032 (green) ( ) RAL ........ ( ) stainless steel design ( ) Flush Mounting: ( ) alpine white in switch range ST 550 by Jung ( ) stainless steel in switch range LS stainless steel by Jung. ( ) pure white in switch range E2 by Gira for FM installation 62.5 deep FM sockets are required |
|  | ......................... pc € .............................. € .............................. Repeater to extend bus length by another 900m. To mount on standard mounting rails. Operating voltage: 10 – 32V DC Current consumption: 80mA (at 24 V DC) To achieve star or tree structures more than one repeater and mounting rail connectors are required. Dimensions (WxHxD): 35.2 x 66 x 102.6 mm Enclosure rating: IP 20 |
|  | ......................... pc € .............................. € .............................. Housing AP housing with top hat rails to take up to 5 repeaters and power supply. Dimensions (WxHxD): 300 x 150 x 120 mm (ID-103978) |
|  | ......................... pc € .............................. € .............................. Power supply to supply up to 5 repeaters Supply voltage 230 V AC, operating voltage 24 V DC Output current: 1.25 A (ID-127066) |
|  | ......................... pc € .............................. € .............................. Mounting rail connector For mounting rail power supply, gold-plated contacts, for mounting on mounting rails, 5 pole. For connection between repeaters. |
|  | ......................... pc € .............................. € .............................. GEZE Service Terminal ST 220 – handheld device for convenient commissioning, service and maintenance of the GEZE SecuLogic rescue route system. Integrated IrDA interface, Plain text display of all events, menu items and adjustments on an illuminated 4-line display, automatic switch-off, membrane keyboard with 5 operating buttons, for battery operation with 4 x AAA batteries. Dimensions (WxHxD): 80x125x37mm Colour: green-blue (similar to RAL 5020) |
|  | ......................... pc € .............................. € .............................. Power supply NET 220 For installation in flush mounted socket plastic housing, moulded module Primary: power supply 230 V AC, 50 Hz Secondary: power supply 24 V DC Power output 500mA, 12W Enclosure rating: IP 54 Dimensions: 50x40 mm (ØxD) |
|  | ......................... pc € .............................. € .............................. Power supply NET 320 For installation in flush mounted socket plastic housing, moulded module Primary: power supply 230 V AC, 50 Hz Secondary: power supply 24 V DC (+/- 5%) Power output 750mA, 18W Dimensions: 55.7 x 33 mm (ØxD) |
|  | ......................... pc € .............................. € .............................. Power supply NT 19.2-24 for wall mounting in plastic housing Primary: power supply 230 V AC Secondary: power supply 24 V DC power output 800 mA, 19.2 W Enclosure rating: IP 54 Dimensions: 100x32x32 mm (WxHxD) |
|  | ......................... pc € .............................. € .............................. NT24-5 power supply in metal housing for DIN rail mounting Primary: power supply 230 V AC Secondary: power supply 24 V DC (adjustable from 24 V to 28 V) power output 5 A, 120 W Enclosure rating: IP 20 Dimensions: 65.5x100x125.2 mm (WxHxD) |