|  | ......................... pcs. .............................. € .............................. € GEZE power supply NT 4.2A-24V HS Power supply for 230V IQ window drives applications For actuation of 24 V IQ window drives an IQ gear and a vent switch are also required. Technical data: Input voltage: 230 V AC Power: 100.8 W Output voltage: 24 - 29 V DC ± 1%, adjustable Output current: 4.2 A Design: Top hat rail casing Dimensions W x H x D [mm]: 100 x 93 x 56 |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE power supply NT 2.5A-24V HS Power supply for 230V IQ window drives applications For actuation of 24 V IQ window drives an IQ gear and a vent switch are also required. Technical data: Input voltage: 230 V AC Power: 60 W Output voltage: 21.6 - 26.4 V DC ± 1%, adjustable Output current: 2.5 A Design: Top hat rail casing Dimensions W x H x D [mm]: 78 x 93 x 56 |
|  | ......................... pcs. .............................. € .............................. € GEZE power supply NT 1.5A-24V HS Power supply for 230V IQ window drives applications For actuation of 24 V IQ window drives an IQ gear and a vent switch are also required. Technical data: Input voltage: 230 V AC Power: 36 W Output voltage: 21.6 - 26.4 V DC ± 1%, adjustable Output current: 1.5 A Design: Top hat rail casing Dimensions W x H x D [mm]: 78 x 93 x 56 |
|  | ......................... pcs. .............................. € .............................. € Power supply NT 1.1A-24V UP Power supply for 230V IQ window drives applications For actuation of 24 V IQ window drives an IQ gear and a vent switch are also required. Technical data: Input voltage: 230 V AC Power: 26.4 W Output voltage: 24 V DC ± 5% Output current: 1.1 A Design: For installation in a deep floating installation box Dimensions: Diameter 54 mm / 32.5 mm high |
|  | ......................... pcs. .............................. € .............................. € IG gear For use 230V IQ window drives applications For supply and actuation of 24 V IQ window drives, 24 V power supply and a vent switch are also required. Technical data: Supply voltage: 24V DC +6V, -4V output signals: Analogue voltage signal for actuating the IQ window drives Design: Dimensions W x H x D [mm]: approx. 20 x 30 x 8 |
|  | ......................... pcs. .............................. € .............................. € GEZE vent switch for ventilation mode ( ) Vent switch LTA-24-AZ with functional keys "On/Off" and LED functional display, protection type IP40, suitable for switch programs with 55x55 mm switching insert. ( ) Surface-mounted ( ) Flush-mounted or ( ) Vent switches can be retrofitted to vent switches LTA-LSA with a rotary button for "On/Off", can also be used as a vent button, protection type IP 40, suitable for switch programs with 55x55 mm switching insert. ( ) Surface-mounted ( ) Flush-mounted Only one switch per IQ gear. |
|  | REMARK Electrical cable laying and connection on site by the electrical company as per the GEZE cable plans. The used cable type should be discussed in collaboration with the acceptance authorities. Configurations with the relevant software can only be carried out by authorised persons. |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |