|  | ......................... pcs. .............................. € .............................. € GEZE indoor climate & building control system Control and operating panel for automated natural ventilation with 4 or 10 potential-free drive outputs. Central unit for operation and parameter setting via real glass, 8.4 inch colour touch display. For flush mounting or installation in cavity walls. Dimensions central unit 270 x 185 x 9 (W x H x set-up depth, mm). Dimensions flush-mounted box 254 x 171 x 85 (W x H x D, mm). Weather station (with wind sensor, heated rain sensor, light sensor, temperature sensor, and GPS receiver). Dimensions of weather station 96 x 177 x 118 (W x H x D, mm). With combi-fixture for installation on wall or mast Wireless interior sensor WGTH-UP for temperature and air humidity. Housing dimensions approx. 55 x 55 x 15 (W x H x set-up depth, mm) for flush wall assembly in standard box Ø 60 mm, 42 mm deep) Central unit with the following connections: 4 or 10 potential-free drive outputs 4 multifunction outputs (for heating, cooling, ventilation system, alarm, light) 4 multifunction inputs (for movement detectors, smoke detectors, closing contact, status messages for a separate air conditioner, automatic reset) 10 connections for external push buttons for the manual, in situ operation of drives and devices Functions Open from a selectable indoor temperature Open from a selectable room humidity Open after CO2 content in room (with optional CO2 sensor) Close when the incoming air temperature is higher than the room ambient temperature Night time back cooling (adjustable period) Daily forced ventilation (adjustable period) External temperature restrictor: Restriction function below a selectable external temperature Keeping closed for an adjustable period Frost alarm: Close during condensation below a selectable external temperature Wind alarm: Close if a selectable wind speed is exceeded Rain alarm: Close during condensation or close to leave a small gap Close when air conditioner is activated Options: ( ) indoor climate & building control system with 4 drive outputs ( ) indoor climate & building control system with 10 drive outputs |
| --- | --- |
| 1.1 | ......................... pcs. .............................. € .............................. € Wireless interior sensor for temperature and air humidity Supplements the GEZE indoor climate & building control system |
| 1.2 | ......................... pcs. .............................. € .............................. € Wireless interior sensor for CO2, temperature, and air humidity Supplements the GEZE indoor climate & building control system |
| 1.3 | ......................... pcs. .............................. € .............................. € KNX interface KNX interface for incorporating the GEZE indoor climate & building control system into the KNX bus system |
| 1.4 | ......................... pcs. .............................. € .............................. € KNX power supply KNX power supply for bus voltage and 24 V DC |
| 1.5 | ......................... pcs. .............................. € .............................. € IQ gear For use for 230V IQ windowdrives applications For supplying and activating the 24 V IQ windowdrives, a 24 V power supply and a vent switch are also required. Technical data: Supply voltage: 24V DC +6V, -4V Output signals: analogue voltage signal for activating the IQ window drives Version: Size W x H x D [mm]: approx. 29 x 25 x 8 |