|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 95 Activation via spring hinge reverser with hand lever For daily aeration and ventilation with vertically installed rectangular windows with bottom-hung, top-hung or side-hung casements, inward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. For window cleaning, the scissors can be disengaged quickly by pressing the release catch. Rod must be covered using an aluminium profile. Clearance-free activation via spring hinge reverser and with hand lever. Technical data: Opening width: 220mm ( ) bottom-hung casement ( ) top-hung casement ( ) side-hung casement Leaf width: ........ mm ( ) 1 scissors for casement widths from 440 - 1100 mm1) ( ) 2 scissors for casement widths from 1101 - 2200 mm1) ( ) 3 scissors for casement widths from 2201 - 2700 mm1) 1) Heed panel widths Casement height: ........ mm (min. 350 mm) Centre of rod to lower edge Hand lever base plate: ........ mm Colour: ( ) silver-coloured EV1 ( ) white, 9016 ( ) RAL shade according to choice Note: When used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm |